## Slide 1: Advanced

## Slide 2: Message Delivery Reliability
at-most-once: At most one message arrives, the message is not copied, there is no duplicate message, but the message may be lost.
at-least-once: At least one message arrives, the message is not lost, but messages can be duplicated.
exactly-once: The message is not copied and lost, no duplicate messages. It means a complete delivery to the consumer for each message given to the mechanism.

## Slide 3
Kafka Ecosystem
Producer
Consumer
Input Systems / Data sources
Output Sinks
KafkaConnect
Source
KafkaConnect
Sink
Mirror Maker
Schema Registry
REST Proxy
Kafka Streams
Notes: The Confluent REST Proxy provides a RESTful interface to a Apache Kafka® cluster, making it easy to produce and consume messages, view the state of the cluster, and perform administrative actions without using the native Kafka protocol or clients.

## Slide 4: Producer Acks
acks = 0 No response expected. There may be data loss. It can be used when collecting logs and metrics. It doesn't matter if a few messages are lost.
acks = 1 Only the leader responds. However, we do not know what the replication is about. There is a risk of data loss, but less than acks=0.
acks = all It waits for the information that all replicas are in place. Warranty increases but performance decreases. It should be set together with min.insync.replicas.
https://www.conduktor.io/kafka/kafka-topic-configuration-min-insync-replicas

## Slide 5: Producer Acks
Default configurations:
  if using Kafka < v3.0, acks=1
  if using Kafka >= v3.0, acks=all
If replication.factor=3, min.insync=2, acks=all
Durability: Tolerate n-1 node down. No data loss.
Availability: The topic must have at least 2 ISR up, and therefore can tolerate at most one broker being down, and we have the guarantee that for every write, the data will be at least written twice.

## Slide 6
KAFKA CLUSTER
Producer Acks
Partition
Message
min.insync.replicas. A value of 2 implies that at least 2 brokers that are ISR (including leader) must respond that they have the data.
Producer
min.insync=2
ACK
NOT_ENOUGH_REPLICAS

## Slide 7: Producer Retries
Developers may need to take some precautions to avoid losing the message when there is an error.
When a message is sent, the Producer that receives a transient failure (e.g. NotEnoughReplicasException) continues to resend it. try.backoff.ms is set per 100 ms.
The limit is 2 seconds, even if the retry is in very high numbers. (delivery.timeouts.ms=120000)
If no response is received within the delivery.timeout period, the sending of that message will be abandoned.
Messages sent with a key may be out of order due to resends. Because there is a parallel transmission. (max.in.flight.requests.per.connection)
https://www.conduktor.io/kafka/kafka-producer-retries

## Slide 8: Idempotent Producer
When the ack doesn’t reach to Producer, Producer resends the message which results duplicate message.
Idempotent Producer solves this (Kafka >= 0.11)
Re-sent requests are sent with the requestid. When Kafka sees the same requestid message, it does not act on it, but still sends an ack.
acks=all
retires=MAX
producerProps.put("enable.idempotence", true);
Kafka >=3.0 it is default.

## Slide 9: Safe Producer (Kafka >= 0.11)
Idempotent Producer
Producer level enable.idempotence=true
Producer/topic level min.insync.replicas=2
There is a cost for Safe Producer

## Slide 10: Message Compression
Messages are compressed at the Producer level. For this, it is not necessary to make an additional setting on the Broker or Consumer side.
compression.type=none/gzip/lz4/snappy.
Messages can be compressed and sent in bulk.
Smaller size, less network occupation, high efficiency, small footprint.
However, it requires a little more processing power.
lz4 might be the optimal choice.
All can be tried.

## Slide 11: Partition Segments
Each partitions has one or more segments (files) covering certain offset range.
Only one segment is active in a partition.
0-1000
1001-2000
2001-?
0-1000
1001-?
0-1100
1101-?
0-1000
2001-?

## Slide 12: Partition Segments
Default size 1 GB. log.segment.bytes
Only one segment is active in a partition.
If no data arrives at the active segment in one week Kafka closes that segment even smaller than 1 GB.

## Slide 13: Segments and Idexes
Each segment has two indexes (files)
First: Position index (offsets)
Second: timestamp index
log.segment.bytes: How many segment will be in a partition.
log.segment.ms: When will the segment will be closed and compaction.

## Slide 14: Log Cleanup
log.cleanup.policiy=delete (Default for all topics)
  Deleted based on time (week)
  Delete based on max size (-1 infinite)
log.cleanup.policy=compact
  Messages deleted by keys
  Removes duplicate key after active segment closed.

## Slide 15: References
https://medium.com/@mehmetbaz/apache-kafka-vs-rabbitmq-82128c579e66
https://www.udemy.com/course/apache-kafka
https://www.amazon.com/Kafka-Definitive-Real-Time-Stream-Processing/dp/1491936169/ref=sr_1_1?dchild=1&keywords=apache+kafka&qid=1613710161&s=books&sr=1-1
https://www.conduktor.io/kafka/kafka-topic-configuration-min-insync-replicas